## Slide 1: Network Layer: Internet Protocol
School of Computer Science Engineering and Technology Bennett University
Greater Noida – 201310

## Slide 2: Outline
Internet Protocol Version 4
Datagram Format, Fragmentation

## Slide 3
Internet Protocol: Requirements
Need
A frame has no routing info. DL layer has no routing info.
For a router with 3+ NIC’s,
how to deliver a packet through multiple links.
How to find a next hop router
Responsibility
Host-to-host delivery
For routing packets through the router and switches.

## Slide 4: Links Between Two Hosts

## Slide 5: Network Layer in an Internetwork

## Slide 6
Network Layer
Source
Creating a packet from the upper layer.
The header contains source and destination IP addresses.
Checking the routing table to find the routing info (eg. Outgoing interface, or machine address of the next hop)
If the packet is larger than MTU, fragment it.
Note that it is different from L4 segmentation/reassembly
Router
Routing the packet by consulting the routing table for each incoming packet and find the i/f that the packet must be sent to.
Destination
Address verification.
For fragmented frames, wait for all fragmentations then reassemble them before delivering the packet to the upper layer.

## Slide 7: Network layer at the Source, Router, and Destination

## Slide 8: IPv4

## Slide 9: IPv4 Datagram Format

## Slide 10: IPv4 Format
Version (4-bit): currently 4.
Header length (4-bit): the length of the IP header in 4-byte unit.
Type of Services(TOS):
This field was not used earlier because of the lack of standard
DiffServ uses this field for differentiate packet types.
Total length:
To define the total length of the datagram including the header in bytes.
16-bit number, the maximum IP size is limited to 216 bytes, or 64 Kbytes.

## Slide 11: IPv4 Format: Fields for Fragmentation
Identification
The source host generates the unique ID
Flags (3-bits) Unused bit
DF bit (Don’t Fragment)
1 – force the router not to fragment the packet. If the packet length is greater than the MTU, the router will discard the packet and send an error message to the source
MF bit (More Fragment)
1 – tell the destination whether or not more fragments follow
Offset
Unit of 8-byte (why?)
Between the beginning of the packet to be fragmented and the beginning of the fragment

## Slide 12: IPv4 Format
Time to Live (TTL)
A packet has a limited lifetime in the network to avoid zombie packets.
Designed to hold a timestamp and decreased by each router. A packet is discarded by a router if TTL is zero.
Revised to hold the maximum number of hops the packet can travel thru the network. Each router decrements it by one.
Protocol
To define payload protocol type
1 for ICMP
2 for IGMP
6 for TCP
17 for UDP
89 for OSPF

## Slide 13: IPv4 Format
Header Checksum
An IP header is slightly modified by each router. At least TTL field.
The checksum must be re-calculated by routers which is a kind of general computers with more than one
network interface.
The checksum must be efficiently calculated with no need of special hardware.
Source IP address and Destination IP address
Options
For new protocols
Padding
To make the header a multiple of 32-bit words

## Slide 14
Example:
An IPv4 packet has arrived with the first 8 bits as shown:
01000010
The receiver discards the packet. Why?

## Slide 15
Solution:
There is an error in this packet. The 4 leftmost bits (0100) show the version, which is correct. The next 4 bits (0010) show an invalid header length (2 × 4 = 8). The minimum number of bytes in the header must be 20. The packet has been corrupted in transmission.

## Slide 16: Example:
In an IPv4 packet, the value of HLEN is 1000 in binary. How many bytes of options are being carried by this packet?

## Slide 17
Solution
The HLEN value is 8, which means the total number of bytes in the header is 8 × 4, or 32 bytes. The first 20 bytes are the base header, the next 12 bytes are the options.

## Slide 18
Example:
In an IPv4 packet, the value of HLEN is 5, and the value of the total length field is 0x0028. How many bytes of data are being carried by this packet?

## Slide 19
Solution:
The HLEN value is 5, which means the total number of bytes in the header is 5 × 4, or 20 bytes (no options). The total length is 40 bytes, which means the packet is carrying 20 bytes of data (40 − 20).

## Slide 20
Example:
An IPv4 packet has arrived with the first few hexadecimal digits as shown.
0x45000028000100000102 . . .
How many hops can this packet travel before being dropped? The data belong to what upper-layer protocol?

## Slide 21
Solution:
To find the time-to-live field, we skip 8 bytes. The time-to-live field is the ninth byte, which is 01. This means the packet can travel only one hop. The protocol field is the next byte (02), which means that the upper-layer protocol is IGMP.

## Slide 22: IPv4: Fragmentation
An IP packet can travel through many different networks using
different L2 (Data Link layers).
The source node has no idea of the path and data link layer its packets will travel.
MTU
Each DL has its own frame format and limitation.
One of such limitation is the maximum size of the frame, which is imposed by software, hardware, performance, and standards.

## Slide 23: IPv4: Fragmentation
MTUs of well known networks.

## Slide 24: IPv4: Fragmentation
The source node usually does not fragment the packet. Instead, L4 will segment the data into a size that can fit into L3 and L2 of the source.
But there is a possibility that a packet travel thru a link whose MTU is smaller than one of the source node.
Then, the packet must be fragmented to go forward the next hop.
Each fragment has its own header mostly repeated from the original packet.
A fragmented packet can be further fragmented into even smaller packet.
Fragmented packets will be re-assembled only by the destination. Why?

## Slide 25: Fragmentation Offset

## Slide 26: Multilevel Fragmentation

## Slide 27
Example:
A packet has arrived with an M bit value of 0. Is this the first fragment, the last fragment, or a middle fragment? Do we know if the packet was fragmented?

## Slide 28
Solution:
If the M bit is 0, it means that there are no more fragments; the fragment is the last one. However, we cannot say if the original packet was fragmented or not. A non-fragmented packet is considered the last fragment.

## Slide 29
Example:
A packet has arrived with an M bit value of 1. Is this the first fragment, the last fragment, or a middle fragment? Do we know if the packet was fragmented?

## Slide 30
Solution:
If the M bit is 1, it means that there is at least one more fragment. This fragment can be the first one or a middle one, but not the last one. We don’t know if it is the first one or a middle one; we need more information (the value of the fragmentation offset).

## Slide 31
Example:
A packet has arrived with an M bit value of 1 and a fragmentation offset value of 0. Is this the first fragment, the last fragment, or a middle fragment?

## Slide 32: Solution:
Because the M bit is 1, it is either the first fragment or a middle one. Because the offset value is 0, it is the first fragment.

## Slide 33: Example:
A packet has arrived in which the offset value is 100. What is the number of the first byte? Do we know the number of the last byte?

## Slide 34
Solution:
To find the number of the first byte, we multiply the offset value by 8. This means that the first byte number is 800. We cannot determine the number of the last byte unless we know the length.

## Slide 35
Example:
A packet has arrived in which the offset value is 100, the value of HLEN is 5, and the value of the total length field is 100. What are the numbers of the first byte and the last byte?

## Slide 36
Solution:
The first byte number is 100 × 8 = 800. The total length is 100 bytes, and the header length is 20 bytes (5 × 4), which means that there are 80 bytes in this datagram. If the first byte number is 800, the last byte number must be 879.

## Slide 37
Example:
A 1440-byte packet that must be routed through an interface with an MTU of 576 bytes (the packet size all hosts should be prepared to accept to comply with the IP RFC). We’ll assume the smallest possible IP header size of 20 bytes meaning the original packet contains 1420 bytes of data. Evaluate total number of fragments, MF field of each fragment, total length field of each fragment and offset value at each fragment.

## Slide 38: Solution:
Fragment | Identificati on | Flags | Fragment Offset | Total Length
One | XXX | 1 | 0 | 572
Two | XXX | 1 | 69 | 572
Three | XXX | 0 | 138 | 336

## Slide 39
Example:
An IP router with a Maximum Transmission Unit (MTU) of 1500 bytes has received an IP packet of size 4404 bytes with an IP header of length 20 bytes. The values of the relevant fields in the header of the third IP fragment generated by the router for this packet are
(A) | MF | bit: | 0, | Datagram | Length: | 1444; | Offset: | 370
(B) | MF | bit: | 1, | Datagram | Length: | 1424; | Offset: | 185
(C) | MF | bit: | 1, | Datagram | Length: | 1500; | Offset: | 37
(D) | MF | bit: | 0, | Datagram | Length: | 1424; | Offset: | 2960

## Slide 40
Solution:
Number of packet fragments = ⌈ (total size of packet)/(MTU) ⌉
= ⌈ 4404/1500 ⌉
= ⌈ 2.936 ⌉
= 3
So, datagram with data 4404 byte fragmented into 3 fragments.
The first frame carries bytes 0 to 1479 (because MTU is 1500 bytes and HLEN is 20 byte so the total bytes in fragments is maximum 1500-20=1480). the offset for this datagram is 0/8 = 0.
The second fragment carries byte 1480 to 2959. The offset for this datagram is 1480/8 = 185.finally the third fragment carries byte 2960 to 4404.the offset is 370.and for all fragments except last one the M bit is 1.so in the third bit M is 0..

## Slide 41: IPv4 Checksum
Only for the header, but not for the payload
Each router modifies the IP header, but not the payload.
No special hardware can be used.
Computationally efficient.
The upper layers will check the integrity of the payload by their own schemes.

## Slide 42: IPv4 Checksum Example

## Slide 43: Thank You